## Slide 1: Balancing Surface and Groundwater Supplies
Groundwater Management Districts Association – Winter Conference
January 7, 2015
Michael J. Lacey, Director
Arizona Department of Water Resources

## Slide 2: ADWR’s Role & Scope
Administers the state’s water laws, explores methods of augmenting water supplies to meet future demands, and works to develop public policies that promote conservation and equitable distribution of water
Innovative system of laws, rules and management authorities that differ for each type and source of water that has supported Arizona’s Economic Development
Bifurcated system where surface water is regulated separately from groundwater
Title 45 of the Arizona Revised Statutes

## Slide 3: ADWR’s Critical Functions
Colorado River Management
Administer Assured and Adequate Water Supply Program
Administer Recharge and Recovery Program
Administer Groundwater Rights and Surface Water Rights Programs
Statewide Regional Planning
Represents the State of Arizona in Indian Water Rights Settlements
Dam Safety and Flood Mitigation
Hydrology

## Slide 4: Sources of Water In Arizona
Groundwater
Surface Water
Colorado River Water
    Main Stem
    Central Arizona Project
Reclaimed Water

## Slide 5: Arizona’s Water Supply Annual Water Budget
Water Source | Million Acre-Feet (maf) |  | % of Total
SURFACE WATER |  |  | 
Colorado River |  | 2.8 | 39.4 %
CAP | 1.6 |  | 22.5%
On-River | 1.2 |  | 16.9%
In-State Rivers |  | 1.4 | 19.7%
Salt-Verde | .9 |  | 12.7%
Gila & others | .5 |  | 7.0%
GROUNDWATER |  | 2.7 | 38.0%
RECLAIMED WATER |  | 0.2 | 2.8%
Total |  | 7.1 maf | 
Source: ADWR, 2014

## Slide 6: Surface Water Management
Definition: “waters of all sources, flowing in streams, canyons, ravines or other natural channels, or in definite underground channels, whether perennial or intermittent, floodwaters, wastewater, or surplus water, and of lakes, ponds, and springs on the surface” (A.R.S. § 45-141)
Doctrine of prior appropriation governs use
Pre - June 12, 1919 Process
Public Water Code (1919)

## Slide 7: Public Water Code
Enacted on June 12, 1919
Provides that a person must apply for and obtain a permit in order to appropriate surface water
    Pre-1919 Statement of Claim
    Post-1919 Statutory Permit
    Stockpond Registration
    Sever and Transfers
Court Decreed
Federal Reserved Right (Winters Rights)
The Adjudication

## Slide 8: Beneficial Uses
Basis, Measure and Limit to the use of water
Beneficial uses are:
  domestic (which includes the watering of gardens and lawns not exceeding one-half acre),
  municipal
  irrigation
  stockwatering
  recreation
  wildlife including fish
  Non-recoverable water storage
  mining

## Slide 9: Colorado River Basin
Approx. 1,400 miles
Connecting Seven States and the Country of Mexico
Drainage of approximately 242,000 square miles
Serves approximately 40 million people
Irrigates approximately 5 million acres of land
Historic Flows between 5MAF and 25MAF
Average Annual Flow 15MAF
Governed By “The Law of the River”

## Slide 10: Law of the River
1922 - Colorado River Compact
1928 - Boulder Canyon Project Act
1929 - California Limitation Act
1931 - Seven Party Agreement (California)
1944 - Arizona Contract for Delivery of Water
1944 - Mexican Water Treaty
1948 - Upper Colorado River Basin Compact
1956 - Colorado River Project Storage Act
1964 - AZ. v. CA. Decree
1968 - Colorado River Basin Project Act
1970 - Criteria for Coordinated Long-Range Operation of Colorado River Reservoirs
1972 - Grand Canyon Protection Act
1973 - Minute 242*
1974 - Salinity Control Act
2001 - Colorado River Interim Surplus Guidelines
2007 - Colorado River Interim Guidelines for Lower Basin Shortages and the Coordinated Operations of Lake Powell and Lake Mead
2012 - Minute 319*
* Part of the 1944 Water Treaty with Mexico. There are also several other Minutes that are part of the Law of the River

## Slide 11
Upper Basin (7.5 maf)
Lower Basin (7.5 maf)
CA – 4.4 maf
AZ – 2.8 maf
NV – 0.3 maf
Mexico 1.5 maf
Arizona Upper Basin – 50 kaf
Colorado River Allocations
UPPER
BASIN
LOWER
BASIN

## Slide 12: Colorado River Management Programs Overview
Entitlement Oversight
    Monitors mainstem Colorado River and Central Arizona Project entitlements and recommends allocations and transfers of these water supplies.
Planning & Operations
    Collaborates with the federal government, and representatives of the seven basin states to better prepare for Arizona’s long term needs and by taking an active role in water use projections, monitoring of hydrologic conditions and hydroelectric projects.
Environmental Programs
    Participates in programs such as the Lower Colorado River Multi-Species Program, the Glen Canyon Dam Adaptive Management Program and the Colorado River Basin Salinity Control Forum.
Bi-National Negotiations
    Represents the State in comprehensive binational partnership for management of Colorado River resources.

## Slide 13: Groundwater Management Statewide Provisions
New Wells - Must file an “Notice of Intent” before drilling any well
Licensing of Well Drillers
Registration of all wells
Groundwater Transportation Protections
Underground Storage & Recovery
Community Water Systems Reporting & Planning
Notes: 13

## Slide 14: Groundwater Management Act
  Passed in 1980
  Created Arizona Department of Water Resources
  Goals of the Groundwater Management Act:
        Control severe groundwater depletion
        Provide the means for allocating Arizona's limited groundwater resources to most effectively meet the state's changing water needs
        Augment Arizona’s groundwater supplies through development of additional water supplies
        Preserve groundwater for use in drought

## Slide 15: Groundwater Management
  Active Management Areas (AMAs)
    Phoenix
    Pinal
    Prescott
    Tucson
    Santa Cruz
Irrigation Non-Expansion Areas (INAs)
    Harquahala
    Douglas
    Joseph City

## Slide 16: Active Management Areas
Five Active Management Areas
  Highest degree of regulation in State
  Management Goals & Planning - Mandatory conservation requirements for most users (municipal, agricultural and industrial)
  Need withdrawal authority to pump >35 gallons per minute
  Must measure and report water use >35 gallons per minute
  New “Non-Exempt” wells may require hydrologic impact analysis
    Well spacing rules

## Slide 17
Phoenix AMA: To achieve safe-yield by the year 2025
Pinal AMA: To preserve agricultural economy for as long as feasible, while considering the need to preserve groundwater for future non-irrigation uses
Prescott AMA: To achieve safe-yield by the year 2025
Tucson AMA: To achieve safe-yield by the year 2025
Santa Cruz AMA: To maintain a safe-yield condition in the active management area and to prevent local water tables from experiencing long term declines
Active Management Area Goals

## Slide 18: Irrigation Non-Expansion Areas
Three Irrigation Non-Expansion Areas
  Harquahala, Douglas and Joseph City
  Groundwater depletion is not as severe as AMAs but requires further regulation
No new irrigated lands
  Substitution of acres possible

## Slide 19: Grandfathered Groundwater Rights
Based on historic pumping (1975-1979)
Irrigation grandfathered rights
Type 1 non-irrigation grandfathered rights
      Converted from an Irrigation GFR
Type 2 non-irrigation grandfathered rights
      Based on historic pumping for a non-irrigation purpose
      Portable within AMA of Origin

## Slide 20: Service Area Rights
City/town/private water company/irrigation districts: Pumping and Delivery to Non-Irrigation Customers
Untreated water provider: Pumping and Delivery to Landscapes Via Non-Potable Distribution System
Expandable Rights: Grow to Serve Service Area Population

## Slide 21: Assured Water Supply Program
Inside Active Management Areas
Established in 1980
Rules adopted in 1995
Arizona Department of Real Estate cannot issue Subdivision Plats without 100-year AWS Demonstration
  Certificates of Assured Supply
  Service by water provider with Designation of Assured Supply
Public Notice Process
  Certificates
  Designations
On-Line Application Status

## Slide 22: Adequate Water Supply Program
Outside the Active Management Areas
Established in 1973
Consumer advisory program
  Plats can be approved with inadequate determination. Disclosure of inadequate water supply required to first buyer
  Water Reports
  Service by water provider with Designation of Adequate Supply
Required Public Notice Process
  Designations of Adequacy
  Water Reports
On-Line Application Status

## Slide 23: Underground Storage and Recovery Program
Recharge
    Storing excess water supplies for future use
Underground Water Storage and Recovery (1986)
Underground Storage and Recovery Act (1994)
    Consolidated Programs
Types of Storage
    Annual Storage & Recovery
    Long Term Storage
Sources of Stored Water
    Reclaimed
    Central Arizona Project
    Surface Water
91st Ave Wastewater Treatment Plant

## Slide 24: QUESTIONS?

## Slide 25: ARIZONA’S NEXT CENTURY Strategic Vision for Water Supply Sustainability
Groundwater Management Districts Association – Winter Conference
January 7, 2015
Michael J. Lacey, Director
Arizona Department of Water Resources

## Slide 26: What We Have Accomplished
Chart: Arizona Water Use, Population and Economic Growth (1957 – 2010)
| 1957 | 1973 | 1980 | 1990 | 2000 | 2010 | 2011
Adjusted GDI | 11.9887 | 37.0453 | 54.3295 | 85.6839 | 152.9337 | 196.193
Population | 1.125 | 2.1253 | 2.7378 | 3.6841 | 5.1606 | 6.4132
Water Use (AF) | 7.1 | 8.2 | 10 | 9.1 | 7.6 | 7.1

## Slide 27: What We Have To Address
Chart: Water Demand (Acre-Feet)
Baseline Demand | 7103425.068 | 7103425.068 | 7103425.068 | 7103425.068
Projected New Demand (Low Industrial) | 0 | 1087765.8118 | 1534013.1687 | 2827203.022
Additional Projected Demand (High Industrial) | 0 | 404075.34 | 455549.2478 | 588255.153
Mid Range Projected Population | 6628756.8 | 10453870.3 | 13252012.8 | 18322751
Source: WRDC, 2011

## Slide 28: What We Are Doing Arizona Strategic Vision for Water Supply Sustainability
Purpose:
Identify viable strategies to guide Arizona in addressing future water needs, providing a stable economy for our future – for all water users.
Uses existing information (CRBS, WRDC, Az. Water Atlas, Water Level Monitoring, AMA Assessments)
Identify Local Options First
Identify Priority Strategies

## Slide 29
Arizona’s Strategic Vision | 
Water Supply and Demand Analysis | 
Arizona (2010) Water Resources Development Commission | Total statewide demands Current - 6.9 MAF 2035 - 8.1 MAF 2110 - 10.6 MAF Projected imbalance between 900,000 and 3.2 MAF over the next 25 to 100 years
Reclamation (2012) Colorado River Basin Water Supply & Demand Study | Colorado River Basin-Wide average imbalance of 3.2 MAF by 2060 Arizona’s projected imbalance between 260,000 to 1.4 MAF by 2060

## Slide 30: Arizona’s Strategic Vision Water Supply Opportunities
Non-Indian Agricultural (NIA) Priority CAP water
Reclaimed Water/Water Reuse
Groundwater in storage
  potable, poor quality & brackish supplies
Water Supply Development
  Revised Watershed Management Practices
  Weather modification
  Rainwater Harvesting/Stormwater Capture (large-scale or macro)
Importation or Exchange of New Water Supplies Developed Outside of Arizona (e.g., Ocean Desalination)

## Slide 31: Arizona’s Strategic Vision Challenges
Complex Physical Water Supply Availability
Land Ownership
  69% of Lands in Arizona Federally Owned & Managed
    Federal Reserve Rights
    Access to Water Supplies and Transmission of Future Water Supplies
    NEPA/ESA/CWA Compliance
General Stream Adjudication
Outstanding Tribal Water Rights Claims
Complex Water Rights System

## Slide 32: Arizona’s Strategic Vision Strategic Priorities For Moving Arizona Forward
  Identify the Role of In-State Water Transfers
  Resolution of Federal and Non-Federal Water Rights Claims
    General Stream Adjudication
    Indian Water Rights Settlements
  Continued Commitment to Water Conservation & Reuse of Reclaimed Water – Including Direct Potable Reuse
  Comprehensive Statewide Data Collection & Analysis
    Modeling Local Conditions
  Supply Importation - Desalination
  Funding
    Rural Infrastructure
    Business, Community and State Leader Engagement

## Slide 33: Arizona’s Strategic Vision Roll Out Process
Whistlestop Tour (46 So Far)
  GUACs Watershed Groups Water Users/Associations
  ITCA IBWC SE AZ Community Forum Homebuilder Reps
  AHS AZ House & Senate Chambers of Commerce
  WRRC Agribusiness & Water Council Arizona Congressional Delegation
Topic Specific Engagement
  Desalination
    Design Build Finance Reps Mexican Water Officials
  Water Transfers
    DCDC Dialogue – ADWR / Yuma Reps
  Reuse
  Adjudication Process
  Economic Development/Finance Alternatives
Next Steps Planning - Integration

## Slide 34: Arizona’s Strategic Vision Conclusions
Ultimately, the State of Arizona is not facing an immediate water crisis
  There are some local areas that require more immediate action
Growing statewide imbalance between existing water supplies and demand projected in the next 25 years
The lack of an immediate problem increases the potential for inaction
Arizona’s History is its Future!
  We must continue to invest and develop new water supplies and infrastructure to support economic growth
Arizona needs a continuing Strategic Vision for Water Supply Sustainability to guide its economic stability through the next century

## Slide 35: Arizona’s Strategic Vision for Water Supply Sustainability
Questions?
Michael J. Lacey
Director
mjlacey@azwater.gov
Phone: (602) 771-8426