## Slide 1
A Quick Look at the 2017 Water Level
Results and Other Aquifer Properties
Geohydrology Section Kansas Geological Survey
University of Kansas
Southwest Kansas GMD #3 Annual Meeting
March 8th, 2016

## Slide 2: Cooperative Water Level Network
Kansas Geological Survey
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 3: Average Change (by well)
Kansas Geological Survey
*Results are based only on the cooperative network (KGS and KDA-DWR) and do not include sub-regional networks from the KGS, KDA-DWR, KGS, or local GMDs. 2017 water levels are provisional.
Region | 1996_1997 | 1997_1998 | 1998_1999 | 1999_2000 | 2000_2001 | 2001_2002 | 2002_2003 | 2003_2004 | 2004_2005 | 2005_2006 | 2006_2007 | 2007_2008 | 2008_2009 | 2009_2010 | 2010_2011 | 2011_2012 | 2012_2013 | 2013_2014 | 2014_2015 | 2015_2016 | 2016_2017
GMD #1 | -0.11 | 0.53 | -0.68 | -0.39 | -0.55 | -0.72 | -1.49 | -0.99 | 0.18 | -0.38 | -0.73 | -1.15 | -0.27 | -0.39 | -0.81 | -1.24 | -1.66 | -0.72 | -0.67 | -0.01 | -0.68
GMD #2 | 0.03 | 1.25 | 0.24 | 0.22 | -0.88 | -0.99 | -0.61 | -0.18 | 0.88 | -0.05 | -2.20 | 1.87 | 1.59 | -0.19 | -0.71 | -3.02 | -1.64 | 2.68 | -1.22 | 1.44 | 2.10
GMD #3 | -0.49 | -0.13 | -1.24 | -0.84 | -2.21 | -1.99 | -3.24 | -1.88 | -0.41 | -1.23 | -2.41 | -1.98 | -2.95 | -1.50 | -3.17 | -3.78 | -3.56 | -2.46 | -2.10 | -1.04 | -1.09
GMD #4 | -0.39 | -0.20 | -0.23 | 0.06 | -1.08 | -0.47 | -1.49 | -1.28 | -0.48 | -0.58 | -0.28 | -0.93 | -0.33 | 0.05 | -0.50 | -0.56 | -1.38 | -0.71 | -0.43 | -0.58 | -0.51
GMD #5 | 0.87 | 1.04 | -0.12 | -0.08 | -0.50 | -0.65 | -1.56 | -1.01 | 0.13 | -0.11 | -1.18 | 3.15 | 0.57 | 0.62 | -0.49 | -2.84 | -1.85 | 0.53 | -0.72 | -0.25 | 0.58
Entire Network | 0.10 | 0.24 | -0.46 | -0.33 | -1.19 | -1.00 | -1.93 | -1.19 | -0.15 | -0.56 | -1.17 | -0.13 | -0.73 | -0.23 | -1.23 | -2.11 | -2.06 | -0.92 | -0.94 | -0.39 | -0.21
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 4: Average Change (by well)
*Results are based only on the cooperative network (KGS and KDA-DWR) and do not include sub-regional networks from the KGS, KDA-DWR, KGS, or local GMDs. 2017 water levels are provisional.
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 5
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 6: Percent Departure from Normal Precipitation
Kansas Geological Survey
Source- National Oceanic and Atmospheric Administration (NOAA)
2016

## Slide 7
March
April
June
July
May
August
2016

## Slide 8
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 9: Simple Water Balance Equation
Kansas Geological Survey
Water Volume Change in Aquifer =
Inflows into Aquifer – Outflows from Aquifer
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Transpiration
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 10: Focusing on Net Inflow and Pumping
Kansas Geological Survey
Water Volume Change in Aquifer =
Inflows into Aquifer – Outflows from Aquifer
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Water Volume Change in Aquifer =
Net Inflow – Pumping
Net Inflow
Transpiration
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 11: Isolating Change from Water Level Volume
Kansas Geological Survey
Water Volume Change in Aquifer =
Net Inflow – Pumping
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Water Level Change x Area x Specific Yield =
Net Inflow – Pumping
Transpiration
Net Inflow
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 12: Isolating Water Level Change
Kansas Geological Survey
Water Level Change x Area x Specific Yield =
Net Inflow – Pumping
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Water Level Change =
(Net Inflow / Area x Specific Yield) –
(Pumping / Area x Specific Yield)
Transpiration
Net Inflow
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 13: Isolating Water Level Change
Kansas Geological Survey
Water Level Change =
(Net Inflow / Area x Specific Yield) –
(Pumping / Area x Specific Yield)
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Water Level Change ≈ b – a * Pumping
Transpiration
Net Inflow
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 14: Thomas County Index Well
Kansas Geological Survey
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 15: Water Level Change and Pumping Best Fit Line
Kansas Geological Survey
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 16: Groundwater Management Districts
Kansas Geological Survey

## Slide 17: Water Use vs Water Level Change, GMD #4
Kansas Geological Survey

## Slide 18: Water Use vs Water Level Change, GMD #4
Kansas Geological Survey

## Slide 19: Water Use vs Water Level Change, GMD #3
Kansas Geological Survey

## Slide 20: Water Use vs Water Level Change, GMD #3
Kansas Geological Survey

## Slide 21
0.4
0.0
2.1
32
17
34
69
28
31
42
35
30
37
38
30
20
2.6
19
19
5.4
2.8
1.4
5.7
7.3
7.3
13
6.4
1.9
Percent Reduction in Pumping to Achieve Q Stable (1998 to 2014)
Mean of values for continuous and maximum wells for 1998-2014 where R2 >0.24 for both or >0.2 for one and >0.3 for the other

## Slide 22: Measured Water Levels, 2005-2016
Kansas Geological Survey

## Slide 23: Water Use vs Water-level Change- All Continuous Wells
Kansas Geological Survey

## Slide 24: Water Use vs Water-level Change- All Continuous Wells
Kansas Geological Survey
2010
(2010 – 2011)

## Slide 25: Percent Departure from Normal Precipitation, 2010
Kansas Geological Survey
Water Year (October 1)

## Slide 26: Monthly Percent Departure from Normal Precipitation, 2010
Kansas Geological Survey
July
August
September
October
November
December

## Slide 27: Water Use vs Water-level Change- All Continuous Wells
Kansas Geological Survey
2010
(2010 – 2011)

## Slide 28: Water Use vs Water-level Change- All Continuous Wells
Kansas Geological Survey
2010
(2010 – 2011)
2011
(2011 to 2012)

## Slide 29: Water Use vs Water-level Change- All Continuous Wells
Kansas Geological Survey
2010 and 2011 Excluded or Averaged

## Slide 30: Q Stable Computed Results
Kansas Geological Survey
26 to 40% reduction in average use = Stable water levels = Sustainable
20% reduction in average use = 0.75 to 1.8 ft declines = decline reduced 50 to 76%
10% reduction in average use = 1.9 to 2.7 declines = decline reduced 24 to 38%
Average Groundwater Use = ~115,000 AF
Average Water Level Decline = ~ 3.3 ft

## Slide 31: SD 6 Local Enhanced Management Area
Kansas Geological Survey

## Slide 32: Water Use vs Water Level Change, Pre-SD 6
Kansas Geological Survey

## Slide 33: Water Use vs Water Level Change, with SD 6
Kansas Geological Survey

## Slide 34: Water Use vs Water Level Change, SD 6
Kansas Geological Survey

## Slide 35: Questions????
Visit our site at http://www.kgs.ku.edu
Kansas Geological Survey
1930 Constant Ave
Lawrence, KS 66047
785-864-2118
Notes: Thank You!

## Slide 36: Isolating Water Level Change
Kansas Geological Survey
Water Level Change x Area x Specific Yield =
Net Inflow – Pumping
Inflow
Outflow
Recharge
Pumping Well
Streambed
Interactions
Return Flows
Water Level Change =
(Net Inflow / Area x Specific Yield) –
(Pumping / Area x Specific Yield)
Transpiration
Net Inflow
In the Kansas HPA, Net Inflow and Specific Yield change little with time because:
Annually-based data
Seasonally pumped aquifer
Relatively large areas
Significant depths to water
Reliable water–level and water-use data
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.

## Slide 37: Q Stable, by Township, GMD2
Kansas Geological Survey

## Slide 38: Water Use vs Water Level Change, GMD #1
Kansas Geological Survey

## Slide 39: Water Use vs Water Level Change, GMD #1
Kansas Geological Survey

## Slide 40: Water Use vs Water Level Change, GMD #3
Kansas Geological Survey

## Slide 41: Water Use vs Water Level Change, GMD #3
Kansas Geological Survey

## Slide 42: Water Use vs Water Level Change, GMD #5
Kansas Geological Survey

## Slide 43: Water Use vs Water Level Change, GMD #5
Kansas Geological Survey

## Slide 44: Water Use vs Water Level Change, GMD #2
Kansas Geological Survey

## Slide 45: Water Use vs Water Level Change, GMD #2
Kansas Geological Survey

## Slide 46
Notes: Normal precipitation is just the average of the last 30 year decal period. The precipitation patterns in Kansas have a major influences on the both the landscape and associated land use in the state.